## Slide 1: Failure Inference based Fast Reroute with Progressive Link Metric Increments
Srihari Nelakuditi

## Slide 2: Traditional Link State Routing
Advertises link state changes to whole network
Routing table recomputations at each router
Network-wide convergence incurs some delay
  May cause forwarding loops and packet drops
Goal: Loop-free loss-less shortest-path forwarding
Notes: In traditional link state routing, like OSPF, a router advertises any adjacent link state changes to all the routers in its domain.
Each router then independently computes new forwarding tables.
The interval between the time a link’s state changes and the time all the routers have updated their forwarding tables is referred to as convergence delay.
During convergence, due to discrepancies between the views of different routers, there may be forwarding loops and packet drops.
The core issue is how to provide loop-free forwarding along the shortest paths without any packet drops, in the presence of link state changes, which is the focus of this talk.

## Slide 3: Outline
Planned shutdown of links
  Progressive link metric increments
Unplanned failures of links
  Failure inference based fast reroute (FIFR)
Network reconvergence while fast reroute
  FIFR with progressive link metric increments (FIFR++)
Performance evaluation
Conclusions and on-going work
Notes: Here is the outline of the talk.
We consider two possible link state changes.
One is bringing down links for maintenance and the other is unexpected failure of links.
I will talk about a previously proposed approach called progressive link metric increments for graceful shutdown of links.
For dealing with unplanned failures, we proposed a scheme earlier called failure inference based fast reroute.
Then, I will talk about our main contribution in this paper called FIFR++ for providing loop-free convergence while performing fast reroute.
I will present the results of our performance evaluation of FIFR++ and conclude the talk with some of the on-going extensions of this work.

## Slide 4: Planned link shutdown
Links brought down for routine maintenance
Forwarding loops possible during convergence
Notes: Network administrators periodically bring down links for routine maintenance.
They shutdown a link only after all the other routers recompute their forwarding tables diverting traffic away from that link.
But during the convergence process, there could be forwarding loops.

## Slide 5: Forwarding during convergence
1
1
2
2
6
4
4
6
A
X
X
B
C
E
B
E
E
F
D
F
F
 | F
 | F
 | F
 | F
2∞
Notes: Consider this simple topology consisting of 7 routers.
Each link here is labeled with its weight.
Let us assume that the destination is F.
Then, these are the next hops along the shortest paths from each node to destination F
Suppose the link B-E needs to be brought down for maintenance.
B sends the link state advertisement with cost of B-E set to infinity.
Once everyone updates their routing tables, B will shutdown the link.
In the meantime, it will continue to forward the packets over the B-E link.
Suppose no one has updated their routing tables and X has a packet with destination F.
X forwards it to B.
Since B-E link is not shutdown yet, B forwards it to be E, which will send it F.

## Slide 6: Forwarding during convergence
2∞
X
1
1
2
6
4
4
6
A
X
X
B
C
E
B
E
E
F
D
F
F
 | F
 | F
 | F
A
Loop
 | F
Notes: Now suppose X has updated its forwarding table and its new next hop is A.
We say that X is in AC (after change) state and the rest are in BC (before change) state.
Now if X sends the packet to A, it will send it back to X, which will send it A again, causing a loop.

## Slide 7: Planned link shutdown
Links brought down for routine maintenance
Forwarding loops possible during convergence
Graceful shutdown with loop-free convergence
  Ordered FIB updates
Notes: One way to ensure loop-free convergence is to enforce a certain order among the routers to update their FIBs.

## Slide 8: Ordered FIB Updates
2∞
A
X
1
1
2
6
4
4
6
A
X
X
B
C
E
B
E
E
F
D
F
F
 | F
 | F
 | F
A
C
 | F
 | F
Notes: Suppose A updates its forwarding table first and then X updates its table.
Now, if X has a packet to F, it will send it to A.
A will then send it to its updated next hop C.
Thus, the packet goes from X to F without any loops.

## Slide 9: Planned link shutdown
Links brought down for routine maintenance
Forwarding loops possible during convergence
Graceful shutdown with loop-free convergence
  Ordered FIB updates
    Coordination/signaling between routers
  Progressive link metric increments
    No changes needed to the routing protocol
Notes: While this approach guarantees loop-free convergence, it requires coordination between routers to order their updates.
Progressive link metric increments is proposed as a practical alternative that can be readily deployed without any changes to the routing protocol.

## Slide 10: Progressive Link Metric Increments
2
X
1
1
27
2
6
4
4
6
A
X
X
B
C
E
B
E
E
F
D
F
F
 | F
 | F
 | F
 | F
Notes: The core idea of progressive link metric increments is that instead of changing the cost from 2 to infinity, it is done in steps.
In this example, suppose the cost of link is changed from 2 to 7.
Then regardless of the order of updates, there won’t be any forwarding loop.
Once the network converges to B-E cost of 7, then B can advertise the cost of infinity.
Thus, progressive link increments can be used to gracefully shutdown a link.

## Slide 11: Progressive Link Metric Increments
A
1
1
27
2
6
4
4
6
A
X
X
B
C
E
B
E
E
F
D
F
F
 | F
 | F
 | F
 | F
C

## Slide 12: Progressive Link Metric Increments
X
1
1
7∞
2
6
4
4
6
A
X
B
C
E
B
E
E
F
D
F
F
 | F
 | F
 | F
 | F
C
A
7
 | F
Notes: If X and B are in OLD state, packets still go through X-B-E, since it is a planned link down.
Thus, progressive link increments can be used to gracefully shutdown a link.

## Slide 13: Unplanned link failures
Network failures happen fairly frequently
  Faulty interfaces, router crashes, fiber cuts
Increased expectation from the Internet
  Need to provide high availability despite failures
IP fast reroute mechanisms for protection
  Not-Via Addressing
Notes: But what happens if a link fails unexpectedly.
There have been studies that show that link failures are not uncommon.
On the other hand, users expect high network service availability regardless of the failures.
The approaches discussed so far avoid loops but by themselves can not guarantee packet delivery in case of unplanned failures.
There have been several IP fast reroute mechanisms proposed to address this problem.
Among them, one of the popular schemes is called NotVia.

## Slide 14: Not-Via Addressing
 | E\BE
 | F
 | E\BE
 | F
1
1
2
2
6
4
4
6
A
X
B
C
E
B
E
E
F
D
F
F
 | F
X
 | F
 | F
 | F
 | E\BE
 | F
 | E\BE
 | F
 | F
 | E\BE
 | F
Notes: Let us see what happens with NotVia.
Suppose B-E failed and B detects the failure. But all other routers are not informed of the failure.
If X has a packet to F, it sends it to its usual next hop B.
Now B reroutes the packet by encapsulating the original packet in another packet.
The destination address in the outer packet is a special address called NotVia address.
It means that next hop for this address should be computed by excluding the link B-E.
That is why it is called NotVia address.
Each interface has a NotVia address apart from the usual IP address.
Here the destination address is E but NotVia B-E link.
Since the next hop to E without B-E link is X, B sends the packet to X.
All the routers are expected to interpret this address consistently.
So, X sends the packet to A and so on.
Thus the encapsulated packet reaches E.
E decapsulates the packet and forwards the original packet to F.
This is more like tunneling around the failed link.

## Slide 15: Unplanned link failures
Network failures happen fairly frequently
  Faulty interfaces, router crashes, fiber cuts
Increased expectation from the Internet
  Need to provide high availability despite failures
IP fast reroute mechanisms for protection
  Not-Via Addressing
    Encapsulation/decapsulation of IP datagrams
  Failure inference based fast reroute (FIFR)
    No modifications to the IP datagram
Notes: The downside of NotVia is that it requires encapsulation and decapsulation of packets around the failed link.
We proposed an alternative approach called failure inference based fast reroute (FIFR) that does not require any changes to the IP datagram.

## Slide 16: Failure inference based fast reroute
1
1
2
2
6
4
4
6
A
X
B
C
E
B
E
E
F
D
F
F
 | F
 | F
X
A
D
X
 | F
 | F
 | F
 | F
Notes: Under FIFR, apart from the usual next hops, we maintain what we call back hops.
Here, the usual next hop from X to F is B.
But if the packet with destination F arrives at X from B, then it is forwarded to A.
Similarly, usual next hop from A to F is X.
But if the packet to F arrives at A from X, then it is sent to D.
Suppose link B-E failed. B detects and others are unaware.
If X has a packet to F, it will send it to its usual next hop B.
B reroutes the packet to X, since that is the next hop without B-E link.
X will use the backhop and forward it to A.
A again uses the backhop and sends it to D.
Thus, the packet traverses the path XBXADF.
You may be wondering why A sends the packet to D, not C.
In other words, why is the back hop for XA is D not C.
Note that A does not know which link failed. Could be B-E or E-F.
It avoids the farthest link, referred to as the key link, which is E-F in this case, for computing back hop D.
With FIFR, each router effectively performs interface-specific forwarding, i.e., the next hop depends not only on the destination but also previous hop.
The forwarding entries are same for all interfaces except for the interfaces that are along the reverse shortest path to destination.
Since nowadays a copy of the FIB is maintained for each interface, this does not require any changes to the forwarding plane.
The key distinguishing factor is that it guarantees loop-free forwarding to any reachable destination without requiring any changes or carrying any additional information in the packet.

## Slide 17: Network reconvergence + fast reroute
Local reroute is fast but paths are suboptimal
  Need to trigger convergence for optimal routing
Requirements
  Continuous loop-free forwarding
  Minimal convergence delay
  No changes to the IP datagram
  No changes to the routing protocol
Proposal
  FIFR with progressive metric increments (FIFR++)
Notes: Fast reroute schemes work fine in routing around a failed link, but packets may take long detours.
To get back to shortest path forwarding, we need to go through the convergence process while performing fast reroute.
We want this combined approach to satisfy these requirements.
To meet these requirements, we propose FIFR++.

## Slide 18: FIFR without metric increments
X
1
1
2
2
6
4
4
6
A
X
B
C
E
B
E
E
F
D
F
F
X
D
X
 | F
 | F
 | F
 | F
A
A
2∞
Notes: First, let us see what happens if we initiate convergence with FIFR but without incremental updates.

## Slide 19: FIFR without metric increments
1
1
2∞
2
6
4
4
6
A
X
B
C
E
B
E
E
F
D
F
F
A
X
 | F
C
 | F
 | F
 | F
X
A
 | F
Notes: The path taken depends on which routers are updated, but the order of updates does not matter in terms of loop freedom and packet delivery.

## Slide 20: Need for metric increments with FIFR
F
F
A
B
B
C
C
G
G
D
B
E
C
H
F
D
I
E
G
A
E
I
3
2
2
1
2
17
2
9
2
2
1
18
D
E
H
F
D
 | G
 | G
 | G
 | G
 | G
Loop
 | G
 | G
1∞
Notes: But FIFR can cause loops without metric increments. Here is an example.

## Slide 21: No loop with FIFR and metric increments
F
F
A
B
B
C
C
G
G
D
B
E
C
H
F
D
I
E
G
A
E
I
3
2
2
1
2
17
2
9
2
2
1
18
D
E
D
B
C
 | G
111
 | G
 | G
 | G
 | G
 | G
Notes: But with metric increments, we can guarantee loop-free convergence while performing fast reroute.

## Slide 22: No loop with FIFR and metric increments
F
F
A
B
B
C
C
G
G
D
B
E
C
H
G
D
I
E
G
A
E
3
2
2
11
2
17
2
9
2
2
1
18
D
E
H
B
C
 | G
1115
 | G
 | G
 | G
 | G
 | G

## Slide 23: No loop with FIFR and metric increments
F
F
A
G
B
C
C
G
G
D
B
E
C
H
G
H
I
E
A
E
3
2
2
15
2
17
2
9
2
2
1
18
D
E
H
F
C
 | G
1520
 | G
 | G
 | G
 | G
 | G

## Slide 24: No loop with FIFR and metric increments
F
F
A
G
B
A
C
G
G
D
F
E
C
H
G
H
I
E
3
2
2
20
2
17
2
9
2
2
1
18
D
E
H
F
D
 | G
20∞
 | G
 | G
 | G
 | G
 | G

## Slide 25: Need for deferring back hop computation
C
D
A
C
45
B
F
2
F
H
1
H
G
F
8
D
C
1
E
D
3
E
I
6
I
7
1
H
F
5
1
1
1
 | H
 | H
 | H
 | H
 | H
 | H
Loop
G
4
B
Notes: At D, Equal cost paths for DCEFH and DGEFH. Loop occurs in one of the possibilities.
So, we intentionally did not write the other path. (We can say that: this is a very rare possibility).

## Slide 26: No loop with deferred back hop computation
D
A
C
45
B
F
2
F
H
1
H
G
F
8
D
C
1
C
E
D
3
E
I
6
I
7
1
H
F
5
1
1
1
 | H
 | H
 | H
 | H
 | H
 | H
G
4
 | H
B
Notes: At D, Equal cost paths for DCEFH and DGEFH. Loop occurs in one of the possibilities.
So, we intentionally did not write the other path. (We can say that: this is a very rare possibility).

## Slide 28: Performance Evaluation
Various types of topologies
  Rocketfuel topologies (6)
  Internet Zoo topologies (262)
  Random topologies generated using BRITE (14)
Simulated failure of one link at a time
  Verified if a packet from each pair of nodes gets caught in a loop, considering all possible combinations of states nodes can be in

## Slide 29: Metric increments rarely needed with FIFR
Only 3 links out of 282 topologies (42091 links)
Notes: 99% of links do not need incremental updates with FIFR.

## Slide 30: Length of metric sequences

## Slide 31: Application to Software Defined Networks
SDN makes realizing FIFR easier
  Forwarding rules can be based on incoming port
SDN also needs a fast local reroute like FIFR
  During the time between failure and new rules
Loop-free convergence not a concern with SDN
  FIFR++ like approach still helpful as it makes SDN agnostic to the order in which forwarding rules are distributed by controller to switches
Notes: So far, we discussed FIFR++ in the context of traditional link state routing where forwarding table computation is decentralized.
Question is how does it help in the context of software defined networks where the decision making is centralized and controller computes the forwarding rules and distributes them to switches,
First, it is easier to realize FIFR with SDN since forwarding rules can be based on incoming interface and not just the destination address.
Second, even SDN needs a fast reroute mechanism like FIFR during the time between an unexpected failure and the installation of new rules.
Convergence delay is not a major concern with SDN
Order of distribution

## Slide 32: Summary
Benefits of FIFR++
  Links can be shut down immediately
  Protection against any single failures
  No changes to IP datagram or routing protocol
On-going work
  Efficient computation of metric sequences with FIFR
  Validation with node failures also
  Extension to asymmetric link weights
Notes: What about link up event.

## Slide 33
Thank You
ARENA for Research on Emerging Networks and Applications